## Slide 1: Matrix-free algorithms for cardiac simulations
Andrea Tonini, Junxiang Wang, Luca Dede’
8th September 2026

## Slide 2
Introduction
  Motivations
  Matrix-free algorithms
3D-0D electromechanical model
  Electrophysiology model
  Cardiac mechanical model
  0D circulatory model
Poromechanics model
Conclusions and future developments

## Slide 3: Cardiac modeling
World Health Organization: cardiovascular diseases are the leading cause of death globally
Hypertension
Atrial fibrillation
Congenital heart defects
Covid-19
RIGHT HEART:
Atrium
Ventricle
SYSTEMIC
CIRCULATION
PULMONARY
CIRCULATION
LEFT HEART:
Atrium
Ventricle
Simulate accurately the cardiovascular system by means of physics-based mathematical models, in an HPC enviroment

## Slide 4: Matrix-based vs matrix-free
Matrix-based
Matrix-free
Update the in-house lifex library for running cardiac simulations with matrix-free algorithms
We also updated lifex to use SIMD (Single Instruction, Multiple Data) and vectorization
System matrix
Assemble and store
Matrix-vector product
Use stored matrix entries
Time per iteration
High number of
communications between
processors
Scalability
Limited by memory accesses
Matrix-vector product
Compute the matrix
action on the fly
Time per iteration
Repetitions of the
same computations
Scalability
No limitations given by memory accesses
Kronbichler, M. and Kormann, K. (2012)
System matrix
Do not store any matrix

## Slide 5
3D-0D electromechanical model

## Slide 6: 3D-0D electromechanical model
Strains
Cardiac chambers
pressures
Cardiac chambers
volumes
Cardiac
electromechanics
Ionic
activity
Electrical
activity
Force
generation
Mechanics
Circulation
Cardiac chambers
pressures
Ionic currents
Potential
Active tension
Deformed sarcomere length
Strains
Calcium
Cardiac chambers
volumes
Matrix-free :work in progress
Fedele, M. et al. (2023)

## Slide 7: Electrophysiology
Electrophysiology describes cardiac ionic dynamics and electrical propagation
w are the concentrations of ionic species and the gating variables
Ionic model (TTP061):
Monodomain model2: u is the unknown transmembrane potential
Ionic
activity
Electrical
activity
Ionic currents
Potential
1Ten Tusscher, K.H. and Panfilov, A.V. (2006)
2Potse, M. et al. (2006)

## Slide 8: Electrophysiology scalability tests
Solved with CG, tolerance 1e-10, Chebyshev preconditioner
MB: matrix-based
MF: matrix-free
Old: w/o SIMD and vectorization
New: with SIMD and vectorization

## Slide 9: Active force generation and mechanical models
Mechanics
Mechanical model2: d is the unknown displacement
z are the state variables of the active force generation model used to derive the active tension Ta
Active force generation model (RDQ20MF1):
Force
generation
Active tension
Deformed sarcomere length
Deformed sarcomere length (SL)
1Regazzoni, F., Dede’, L. and Quarteroni, A. (2020)
2Guccione, J.M. and McCulloch, A.D. (1991)

## Slide 10: Passive mechanics scalability tests
Solved with GMRES, tolerance 1e-15, Chebyshev preconditioner
MB: matrix-based MF: matrix-free Old: w/o SIMD and vectorization New: with SIMD and vectorization

## Slide 11: 0D circulatory model
Electrical analogy:
Q Flux = current
P Blood pressure
= electric potential
Resistance to blood flow = electric resistance
Vessel compliance
= capacitance
Blood inertia
= inductance
Regazzoni, F. et al. (2022)

## Slide 12: Current status of matrix-free electromechanics solver
Chambers
pressure
Chambers
pressure
Strains
Chambers
volume

## Slide 13: Missing blocks for the electromechanical model
Mechanical feedback to the monodomain model
Coupling of circulation and mechanics
Divergence theorem
Circulation output

## Slide 14
Poromechanics model

## Slide 15: Poromechanics

## Slide 16: Poromechanical Model

## Slide 17: Poromechanical Model

## Slide 18: Poromechanical Model

## Slide 19: Poromechanical Model

## Slide 20: Poromechanical Model

## Slide 21: Poromechanical Model

## Slide 22: Poromechanical Model

## Slide 23: Poromechanical Model

## Slide 24: Poromechanical Model

## Slide 25: Poromechanical Model

## Slide 26: Poromechanical Model

## Slide 27: Poromechanical Model

## Slide 28: Poromechanical Model

## Slide 29: Conclusions and future developments
Conclusions
Matrix-free algorithms provided improvements in the wall time for high polynomial degrees with respect to matrix-based approaches for electrophysiology and mechanical simulations
Matrix-free algorithms exhibit almost ideal strong scalability in pre-exascale frameworks for electrophysiology and mechanical simulations
Fixed-stress splitting gives a stable route to matrix-free coupled poromechanics perfusion.
Future developments
Coupling of the mechanical model with a 0D circulation model to prescribe pressure boundary conditions at the endocardium
Implementation of a mechanical feedback to the electrophysiology model to account for fiber deformation in the conductivity tensor
Scalability tests for electromechanics
Couple electrophysiology, mechanics and perfusion

## Slide 30: References
M. Kronbichler, and K. Kormann, A generic interface for parallel cell-based finite element operator application, Computers and Fluids, 63 (2012), pp. 135-147.
M. Fedele, R. Piersanti, F. Regazzoni, M. Salvador, P. C. Africa, M. Bucelli, A. Zingaro, and A. Quarteroni, A comprehensive and biophysically detailed computational model of the whole human heart electromechanics, Computer Methods in Applied Mechanics and Engineering, 410 (2023), p. 115983.
M. Potse, B. Dube, J. Richer, A. Vinet, and R. M. Gulrajani, A comparison of monodomain and bidomain reaction-diffusion models for action potential propagation in the human heart, IEEE Transactions on Biomedical Engineering, 53 (2006), pp. 2425–2435.
K. H. Ten Tusscher and A. V. Panfilov, Alternans and spiral breakup in a human ventricular tissue model, American Journal of Physiology-Heart and Circulatory Physiology, 291 (2006), pp. H1088–H1100.
J. M. Guccione and A. D. McCulloch, Finite element modeling of ventricular mechanics, Springer, New York, NY, 1991, pp. 121–144.
F. Regazzoni, L. Dede’, and A. Quarteroni, Biophysically detailed mathematical models of multiscale cardiac active mechanics, PLoS computational biology, 16 (2020), p. e1008294.
F. Regazzoni, M. Salvador, P. C. Africa, M. Fedele, L. Dede’, and A. Quarteroni, A cardiac electromechanical model coupled with a lumpedparameter model for closed-loop blood circulation, Journal of Computational Physics, 457 (2022), p. 111083.